## Slide 1: EyeLink and iEye Adaptation
Qingqing Yang, qy775@nyu.edu
Clayspace Lab Meeting

## Slide 2: Contents
EyeLink Tutorial
  Eye-Tracker data
  Code for Setup and Message
iEye Tutorial
  Procedure of data processing
  Adaptation

## Slide 3: Memory Guide Saccade (MGS) Task
Saccade Trajectory
Aligned Saccadic Endpoints
Epoch 1 2 3 4 5

## Slide 4: Eye-Tracker Data
X axis: Right +
Y axis: Down +
Video:
Right --> Left --> Up --> Down
Explanation SR-Research Eyelink(c) gazetrackers
  Sample: pupil size, x & y gaze position (pixel) at each time point
  Event: event type such as start-end of blink, saccade, fixation.

## Slide 5: EyeLink Setup
EyelinkToolbox can be used to create eye-movement experiments and control the SR-Research Eyelink(c) gaze trackers
It’s incorporated into the PsychToolbox (Psychtoolbox-3 – EyelinkToolbox)
It provides a number of wrapper functions to simplify creating an eye-tracking program
The main functionality could be found in demos: EyelinkToolbox/EyelinkDemos

## Slide 6: EyeLink Setup
Initialization
% Provide Eyelink with details about the graphics environment
el=EyelinkInitDefaults(window);
Eyelink('Initialize','PsychEyelinkDispatchCallback’);
Eyelink('command', 'sample_rate = 1000’);
% make sure that we get gaze and event data from the Eyelink
status=Eyelink('command','link_sample_data = LEFT,RIGHT,GAZE,AREA’);
Eyelink('command','file_sample_data = LEFT,RIGHT,GAZE,AREA,GAZERES,STATUS');
Eyelink('command','file_event_filter = LEFT,RIGHT,FIXATION,SACCADE,BLINK,MESSAGE,BUTTON’);

## Slide 7: EyeLink Setup
Calibrate
% Calibration Setup
Eyelink('command', 'enable_automatic_calibration = YES');
Eyelink('command',’calibration_type= HV5’);
% Calibrate the eye tracker
EyelinkDoTrackerSetup(el);
% do a final check of calibration using driftcorrection
EyelinkDoDriftCorrection(el);

## Slide 8: EyeLink Save File
Save data
% get gaze data from EyeTracker
tempedfFile = 'temp.edf';
edfFile='actual_file_name.edf';
Eyelink('openfile',tempedfFile);
% stop Eye Tracker Recording
if is_eyetracker
Eyelink('stoprecording’);
Eyelink('ReceiveFile',tempedfFile,tempedfFile);
movefile(tempedfFile,edfFile);
WaitSecs(3); print(‘Data Trans Completed.’);
Eyelink('Shutdown')
end

## Slide 9: EyeLink Send Message
Send info of experiment epoch, target locations to eye tracker
  During epoch fixed at the center
Eyelink('Message','TarX1 %s', num2str(0));
Eyelink('Message','TarY1 %s', num2str(0));
  During the epoch respond to the target
Eyelink('Message','TarX1 %s', num2str(task.dotXdva{iTrial}));
Eyelink('Message','TarY1 %s', num2str(task.dotYdva{iTrial}));
Send Target Location in the unit of Degree of visual angle

## Slide 10: EyeLink GazeContingent
Send info of experiment epoch, target locations to eye tracker
eye_used= Eyelink('EyeAvailable');
if Eyelink( 'NewFloatSampleAvailable') > 0
evt = Eyelink( 'NewestFloatSample’); % Get most recent sample data (gaze loc, pupil size)
if eye_used ~= -1 % do we know which eye to use yet?
% if we do, get current gaze position from sample
x = evt.gx(eye_used+1); % +1 as we're accessing MATLAB array
y = evt.gy(eye_used+1);
% do we have valid data and is the pupil visible?
if x~=el.MISSING_DATA && y~=el.MISSING_DATA && evt.pa(eye_used+1)>0
mx=x;
my=y;
end
end
end
Notes: % Get available eye
eye_used= Eyelink('EyeAvailable');
if eye_used==el.BINOCULAR % if both eyes are tracked
eye_used=el.LEFT_EYE; % use left eye
end
if eye_used == -1 % dont know which eye is being tracked
eye_used = el.RIGHT_EYE;
end

## Slide 11: EyeLink GazeContingent Cont.
Send info of experiment epoch, target locations to eye tracker
  When subject gazes at an object, it changes color. When gaze moves away, it toggles back
% check for events
evtype=Eyelink('getnextdatatype’);
if evtype==el.ENDSACC % if the subject finished a saccade check if it fell on an object
% check if saccade landed on an object
choice=-1;
noobject=0;
i=1;
while 1
if 1==IsInRect(evt.genx,evt.geny, object(i).rect )
choice=i;
break;
end
i=i+1;
if i>length(object)
noobject=1;
break;
end
end
Notes: % Get available eye
eye_used= Eyelink('EyeAvailable');
if eye_used==el.BINOCULAR % if both eyes are tracked
eye_used=el.LEFT_EYE; % use left eye
end
if eye_used == -1 % dont know which eye is being tracked
eye_used = el.RIGHT_EYE;
end

## Slide 12: iEye Procedure
iEye is a set of command line functions built to translate data from 'raw' format (typically, EDF files) into scored responses on each trial.
clayspacelab/iEye at iEye_ts (github.com)

## Slide 13: iEye Procedure
Preprocessing
ii_preproc.m
ii_import
ii_data
Message events based on .ifg
ii_trim, ii_rescale, ii_invert, ii_censorchans, ii_definetrial
ii_blinkcorrect
% blink correction
ii_params.blink_thresh = 1.5; % PERCENTILE
ii_params.blink_window = [150 50]; % before and after, ms
ii_smooth, ii_velocity
ii_findsaccades, ii_extractsaccades
sacc_dur >= dur_thresh （0.0075） & sacc_amp >= amp_thresh （0.25）
& velocity > = 30 (dva/s)
ii_findfixations

## Slide 14: iEye Procedure
Preprocessing cont.
ii_preproc.m
drift correction – epoch 1 & 2
ii_selectfixationsbytrial
ii_driftcorrect
Epoch 1 2 3 4 5

## Slide 15: iEye Procedure
Preprocessing cont.
ii_preproc.m
calibration – epoch 4
ii_selectfixationsbytrial
ii_calibratebytrial
Epoch 1 2 3 4 5

## Slide 16: iEye Procedure
Score the saccade error
  Extract initial and final saccade eye position during certain response epoch 4
  Targert coordinate in TarX, TarY
  Calculate the Euclidian distance and response time
  Mark bad trials in ii_sess.excl_trial
Epoch 1 2 3 4 5

## Slide 17: iEye Adaptation
Epochs in the main ieye script
Ifg channel num and names
Multi-item: score each target response separately, calibrate for every feedback (Qingqing-Yang-177/iEye_qy-WMLoads at iEye_ts)
Epoch 1 2 3 4 5

## Slide 18: iEye Results

## Slide 19: Thank you!